## Slide 1: Universal Controller For PWM Converters -Using Normalised approach
slide no :1

## Slide 2: Introduction
In today's world, electronic systems often need to operate at different voltage levels.Converters help to convert one level of DC voltage to another and many electronic appliances were depend on the this converters.
Among these, the Buck, Boost, and Buck-Boost converters are the most commonly used. We will find them in mobile chargers, laptops, electric vehicles, solar inverters, and many other systems were there.
Now These converters must produce a steady output voltage
and this converters don’t work on their own — they need a controller to ensure the output voltage remains stable , To do this, we use controllers

## Slide 3: Types of Converters
Buck Converter
Boost Converter
Buck-Boost Converte
1. Buck Converter (Step-Down Converter):
The Buck converter is used when we need to reduce a higher voltage into a lower voltage. For example, if we have a 24V power supply and we want to charge a phone that needs only 5V, a Buck converter will do the job. It works by rapidly turning the input on and off and smoothing the result using components like inductors and capacitors
Real-life uses:
LED light drivers computer power supplies

## Slide 4: 2. Boost Converter (Step-Up Converter):
The Boost converter is the opposite of the Buck — it increases a lower voltage to a higher one. This is useful when the power source doesn’t provide enough voltage on its own. For example, if we have a 3.7V battery but you need 12V to power a motor, a Boost converter makes that possible.
Real-life uses:
Solar panels (to increase voltage for energy storage or usage) Electric vehicles
3. Buck-Boost Converter (Step-Up and Step-Down Converter)
The Buck-Boost converter is used when we need to either increase or decrease the voltage. It gives the flexibility to handle situations where the input voltage is sometimes lower and sometimes higher than the output we want.For example, if a device needs 12V constantly, but the battery sometimes gives 9V and sometimes 15V, the Buck-Boost converter adjusts it to stay at 12V all the time. It gives more flexibility compared to just Buck or Boost alone.
It works by combining the basic working idea of both Buck and Boost converters.
Real-life uses:
Automotive electronics (like dashboards, sensors) IoT and embedded devices with varying supply

## Slide 5: Literature Review
Paper Title | Authors & Year | Key Contributions | Limitations / Gaps
Adaptive Sliding Mode Control Method for DC–DC Converters | Liqun Shen et al., 2015 | Proposed an adaptive sliding mode control for DC–DC converters, enhancing robustness against parameter variations. | Complex design process; implementation may be challenging for varying converter types
An Intelligent Adaptive Control of DC–DC Power Buck Converters | M. A. Abido 2022 | Developed a backstepping controller with a nonlinear disturbance observer and ANN for buck converters, improving voltage regulation under varying loads | Focused solely on buck converters; does not address universality across different converter topologies.
Adaptive Control of DC-DC Converter Based on Hybrid Fuzzy PID Controller | Minh-Duc Pham & Hong-Hee Lee, 2017 | Combined fuzzy logic with PID control for adaptive regulation in DC–DC converters, enhancing performance under load changes. | Limited to specific converter types; lacks a generalized approach for multiple topologies.

## Slide 6: Research gap
While various control strategies have been developed for individual converter types, most existing methods require manual redesign when there is a change in converter topology or circuit parameters. Despite the growing need for flexible systems, there is still no widely adopted control approach that can adapt universally across different DC-DC converters without reconfiguration.
This lack of a unified, parameter-independent controller highlights a critical gap in existing research, especially in practical, simulation-ready implementations that allow users to input converter specs and achieve stable output without additional tuning.

## Slide 7: Problem Statement:
Although DC-DC converters are widely used and well-studied, most existing controller designs are tightly coupled to specific converter parameters such as inductance, capacitance, and load resistance. As a result, whenever these parameters change, or the system switches from one converter type to another (e.g., from Buck to Boost), the controller must be manually redesigned or re- tuned.
This makes the system less scalable, less flexible, and more time-consuming to implement in real-world applications where configurations change frequently — such as in power electronics labs, modular power supplies, or adaptive energy systems.

## Slide 8: Objective The main objective of this project is to design and implement a universal controller that can work across multiple converter types — namely Buck, Boost, and Buck-Boost — without the need for re-tuning or redesigning the controller every time the circuit parameters change.
To make the controller independent of L, C, values using normalization
To allow users to input any converter specs and still get stable performance
To design the controller based on phase margin and bandwidth ratio
To implement the full simulation and response analysis in MATLAB
In simple terms, the objective is to create one controller that fits all, ensuring stable output voltage for any converter configuration and parameter set, with minimal user effort.

## Slide 9: Normalization: In power electronics, the behavior of a converter depends on the physical parameters like inductance (L), capacitance (C), and the input/output voltages. Designing a controller based on these actual values makes it non-transferable to other converters
Normalization is a mathematical technique where all voltages, currents, and time are expressed as dimensionless quantities, scaled using characteristic values of the system.

## Slide 10: Methodology
User Input
The user selects the converter type (Buck/Boost/Buck-Boost) and provides values like input voltage, output voltage, L, C, R, and switching frequency.
Validation & Normalization
The system checks if the parameters are valid. Then, it calculates normalized quantities using base equations.
Controller Design
The user provides performance specs (phase margin, bandwidth ratio). Controller coefficients are calculated using control theory equations.
Simulation Loop
A time-domain simulation is run using normalized differential equations and a digital compensator. Output voltage and duty cycle are updated step-by-step.
Denormalization & Plotting
The output voltage is converted back to actual values and plotted against time

## Slide 11: Results
This is the result we goput while we use input voltage 24v, reuired Output volage 12v and some converter parameter we got the calculted voltage after settling 12v which matches the required output voltage

## Slide 12: Conclusion In this project, a universal controller was successfully designed and implemented for Buck, Boost, and Buck- Boostconverters using a normalized modeling approach. By eliminating the dependency on specific circuit parameters like inductance, capacitance, input voltage, the controller became fully adaptable to a wide range of converter configurations.
The simulation results confirmed that the normalized controller maintained voltage regulation across all converter types, making the solution flexible, scalable, and practical for real-world applications.

## Slide 13: Thank You
CB.SC.U4AIE24023 – KIRUTHIKPRANAV CB.SC.U4AIE24038 – MANIROOP CB.SC.U4AIE24026 – K.SASANK GUPTA CB.SC.U4AIE24060 - VIKRAM